PowerPoint Presentation
Transport Layer: Sliding Window Reliability
Outline
RTT estimation using EWMA
Stop and Wait
Sliding Window Algorithms

---
Transport layer functions
Transport layer functions
- Transport protocol defines the pattern/sequence for end hosts sending packets
- Transport has to deal with a number of things
  - Multiplexing/demultiplexing – ports and message queues
  - Error detection within packets - checksums
  - Reliable, in order delivery of packets - Today
  - Flow control – Today
  - Connection management - TBD
  - Congestion control – TBD
We’re moving toward understanding TCP

---
Methods of Reliability
Methods of Reliability
Packets can be lost and/or corrupted during transmission
  - Bit level errors due to noise
  - Loss due to congestion
Use checksums to detect bit level errors
  - Internet Checksum is optionally used to detect errors in UDP
    - Uses 16 bits to encode one’s complement sum of data + headers
  - When bit level errors are detected, packets are dropped
Build reliability into the transmission protocol
  - Using acknowledgements and timeouts to signal lost or corrupt frame

---
Acknowledgements & Timeouts
Acknowledgements & Timeouts
An acknowledgement (ACK) is a packet sent by one host in response to a packet it has received
  - Making a packet an ACK is simply a matter of changing a field in the transport header
  - Data can be piggybacked in ACKs
A timeout is a signal that an ACK to a packet that was sent has not yet been received within a specified timeframe
  - A timeout triggers a retransmission of the original packet from the sender
  - How are timers set?

---
Acknowledgements & Timeouts

---
Propagation Delay
Propagation Delay
- Propagation delay is defined as the delay between transmission and receipt of packets between hosts
- Propagation delay can be used to estimate timeout period
- How can propagation delay be measured?
- What else must be considered in the measurement?

---
Exponentially weighted moving average RTT estimation
Exponentially weighted moving average RTT estimation
- EWMA was original algorithm for TCP
- Measure SampleRTT for each packet/ACK pair
- Compute weighted average of RTT
  - EstRTT =  x EstimatedRTT +  x SampleRTT
  - where  +  = 1
  -  between 0.8 and 0.9
  -  between 0.1 and 0.2
Set timeout based on EstRTT
  - TimeOut = 2 x EstRTT

---
Stop-and-Wait Process
Stop-and-Wait Process
Sender
Receiver
- Sender doesn’t send next packet until he’s sure receiver has last packet
- The packet/Ack sequence enables reliability
- Sequence numbers help avoid problem of duplicate packets
- Problem: keeping the pipe full
- Example
  - 1.5Mbps link x 45ms RTT = 67.5Kb (8KB)
  - 1KB frames imples 1/8th link utilization

---
Solution: Pipelining via Sliding Window
Solution: Pipelining via Sliding Window
- Allow multiple outstanding (un-ACKed) frames
- Upper bound on un-ACKed frames, called window
Sender
Receiver
T
ime
…
…

---
Buffering on Sender and Receiver
Buffering on Sender and Receiver
- Sender needs to buffer data so that if data is lost, it can be resent
- Receiver needs to buffer data so that if data is received out of order, it can be held until all packets are received
  - Flow control
How can we prevent sender overflowing receiver’s buffer?
  - Receiver tells sender its buffer size during connection setup
How can we insure reliability in pipelined transmissions?
  - Go-Back-N
    - Send all N unACKed packets when a loss is signaled
    - Inefficient
  - Selective repeat
    - Only send specifically unACKed packets
    - A bit trickier to implement

---
Sliding Window: Sender
Sliding Window: Sender
- Assign sequence number to each frame (SeqNum)
- Maintain three state variables:
  - send window size (SWS)
  - last acknowledgment received (LAR)
  - last frame sent (LFS)
- Maintain invariant: LFS - LAR <= SWS
- Advance LAR when ACK arrives
- Buffer up to SWS frames

SWS
LAR
LFS
…
…

---
Sliding Window: Receiver
Sliding Window: Receiver
Maintain three state variables
  - receive window size (RWS)
  - largest frame acceptable (LFA)
  - last frame received (LFR)
Maintain invariant: LFA - LFR <= RWS
- Frame SeqNum arrives:
  - if LFR < SeqNum < = LFA accept
  - if SeqNum < = LFR or SeqNum > LFA discarded
Send cumulative ACKs – send ACK for largest frame such that all frames less than this have been received

RWS
LFR
LFA
…
…

---
Sequence Number Space
Sequence Number Space
SeqNum field is finite; sequence numbers wrap around
Sequence number space must be larger then number of outstanding frames
SWS <= MaxSeqNum-1 is not sufficient
  - suppose 3-bit SeqNum field (0..7)
  - SWS=RWS=7
  - sender transmit frames 0..6
  - arrive successfully, but ACKs lost
  - sender retransmits 0..6
  - receiver expecting 7, 0..5, but receives the original incarnation of 0..5
SWS < (MaxSeqNum+1)/2 is correct rule
Intuitively, SeqNum “slides” between two halves of sequence number space

---
Another Pipelining Possibility:  Concurrent Logical Channels
Another Pipelining Possibility: Concurrent Logical Channels
- Multiplex 8 logical channels over a single link
- Run stop-and-wait on each logical channel
- Maintain three state bits per channel
  - channel busy
  - current sequence number out
  - next sequence number in
Header: 3-bit channel num, 1-bit sequence num
  - 4-bits total
  - same as sliding window protocol
Separates reliability from order

---
Stop & wait sequence numbers
Stop & wait sequence numbers
Sender
Receiver
Sender
Receiver
Sender
Receiver
(c)
(d)
(e)
Simple sequence numbers enable the client to discard duplicate copies of the same frame
Stop & wait allows one outstanding frame, requires two distinct sequence numbers
Frame 0
ACK 0
T
imeout
Frame 0
ACK 0
T
imeout
Frame 0
ACK 0
T
imeout
Frame 0
ACK 0
T
imeout
Frame 0
ACK 0
Frame 1
ACK 1
Frame 0
ACK 0

---
Sliding Window Example
Sliding Window Example
Receiver
Sender
0
1
2
A3
3
4
5
6
A4
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14

---
Sliding Window Summary
Sliding Window Summary
- Sliding window is best known algorithm in networking
- First role is to enable reliable delivery of packets
  - Timeouts and acknowledgements
Second role is to enable in order delivery of packets
  - Receiver doesn’t pass data up to app until it has packets in order
Third role is to enable flow control
  - Prevents server from overflowing receiver’s buffer